Buildserver-endpoint

# Idea and intent
To make better use of the buildserver-monitor, this document describes some upgrades made to the already build system. Consider this a version 2.

By adding some hardware components features are added: a buzzer, a vibration motor and an OLED screen. By changing the behavior in software the buildserver-monitor becomes a buildserver-endpoint: instead of the device polling a Jenkins buildserver it becomes a TCP client which connects to a server application. This server application can use a defined API to send commands to the buildserver-endpoint, things like: turn led 3 on in color blue and with 40% brightness. Or, turn buzzer on for 500 milliseconds, then 500 milliseconds silence and repeat for 10 times.

An example server application is provided to show how this API is used. It can control a single buildserver-endpoint, although other server application may support many clients at once.

# Build Environment
To make development more pleasant a switch from Arduino IDE to PlatformIO is made. PlatformIO is a plugin for Visual Studio Code, a description how to install it can be found here.
The buildserver-endpoint firmware is build using this IDE.

For the example Server application C# is used (on Windows). For this an old version of Visual Studio Community (2013) is used in combination with a single package (MetroModernUI) to make the interface look a bit better.
The intent is for the user to write a server application in the language of choice: this is the fun part as you now have full control of the buildserver-endpoint.